## Slide 1
Homa, in a lab
Testing the Linux kernel module for the Homa transport protocol
homa-lab 0.1.1 · kernel 6.17.8 · HomaModule main @ 65cecd7 · 26 of 26 tests passing
Companion to the lab walkthrough (homa-lab-walkthrough.pdf)
Notes: homa-lab tests the Linux kernel module that implements Homa, a datacenter transport protocol from Stanford designed as an alternative to TCP for remote procedure calls. The lab runs the module on four hosts joined by a switch with real priority queues, and measures what Homa does under load, under incast and under loss.

## Slide 2
What the lab does
Behaviour and correctness, not datacenter benchmarks
Pinned build
Mainline kernel 6.17.8 and a pinned HomaModule commit. One command builds the image and runs the module's 840 unit tests.
A real switch
sw1 shapes each port to 1 Gbit/s with 8 strict priority queues chosen by the DSCP bits Homa sets, or one FIFO.
Homa's own tools
homa_test, the echo server and cp_node from the module's util/, driven over SSH; a Homa dissector for tshark.
26 tests
Robot suites: platform, function v4/v6, the wire, Homa vs TCP, incast, loss recovery, resend timers.
Notes: The four things the lab is built around. It tests behaviour and correctness, not raw performance: these are VMs on one 12-core host, so absolute numbers are not datacenter numbers, but comparisons on the same machines are fair.

## Slide 3
PART 1
Homa for dummies
What problem Homa solves, how it works, and what it costs — no networking background needed.
Notes: This part is for people who don't live in transport protocols. If the audience knows TCP well, it can be skipped to part 2.

## Slide 4
The problem is the slowest message
One click fans out to hundreds of small requests; the page waits for the last answer
1 in 100
messages is slow
× 100
messages per page
63%
of pages are slow
Datacenter traffic is mostly tiny messages — a few hundred bytes — mixed with occasional big transfers. With TCP the tiny ones get stuck in queues behind the big ones.
What has to improve is the tail (the 99th percentile), not the average.
Notes: The key idea: a request to a datacenter service fans out to many servers and finishes only when the slowest answer arrives. If 1 message in 100 is slow and a page needs 100 of them, 1 - 0.99^100 = 63% of pages are slow. So what matters is the tail, the 99th percentile, not the average.

## Slide 5
A road versus a loading dock
Who decides when data moves, and whether small things can overtake
TCP: a single-lane road
Each sender opens a connection and streams bytes. Drivers accelerate until there is a crash (a lost packet), then brake. Queues fill up before anyone slows down. A pizza scooter behind a convoy of trucks waits behind all of them.
Homa: a dock with a dispatcher
Small parcels drive straight in on an express lane. Anyone with a truckload phones ahead; the dispatcher, who sees everything coming, tells each truck when to come — the one with the least left to unload goes first. Nobody crashes into a full queue, and the scooter never waits behind a truck.
Notes: The analogy. TCP: every sender accelerates until something is lost, then brakes; small messages queue behind big ones. Homa: the receiver acts as a dispatcher that sees everything heading its way, and the network has express lanes for small messages.

## Slide 6
How Homa works, in five ideas
1
Messages, not streams
Whole messages in, whole messages out: request + response = an RPC.
2
No connections
One socket talks to thousands of peers with no setup or teardown.
3
Small messages just go
Up to ~40 KB is sent at once; a longer message is announced and waits.
4
The receiver dispatches
It grants permission to send, closest-to-finishing first.
5
Express lanes in the switch
Each packet carries a priority 0–7; switches serve 7 first.
Notes: The five ideas, in order. Note idea 3 in this module version: messages up to about 40 KB go immediately; since September 2026 a longer message is announced with START_MSG and every byte waits for a grant.

## Slide 7
What Homa gives you
Low tail latency
Papers report 10–100× lower p99 for short messages under load than TCP.
No head-of-line blocking
Messages are independent; one slow message doesn't hold up the rest.
Incast by design
When 100 servers answer at once, the receiver lets them in a few at a time.
Scales to many peers
No connection per pair: no handshakes, no connection tables.
Fits RPC software
Gives frameworks messages directly instead of a byte stream.
Uses existing hardware
Switch priority queues already exist; they just need configuring.
Notes: Benefits. The 10-100x figure is the Homa authors' measurement on real datacenter hardware; the lab reproduces the direction of the effect at small scale: under incast, Homa's short messages stayed under 2 ms at p99 while TCP's took 20-40 ms.

## Slide 8
What it costs
Not in Linux yet
Out-of-tree module tied to kernel versions; upstreaming in stages since 2024.
Apps must change
Message API, mapped receive buffers, 1 MB limit. Not a drop-in for TCP.
Datacenter only
No encryption; NAT, firewalls and load balancers don't know protocol 146.
Needs switch config
Without priority queues much of the benefit is gone.
Offloads are for TCP
NICs don't segment Homa; TCP was faster for big transfers here.
Big messages can starve
Shortest-first favours small ones; the FIFO-share knob is off by default.
Tuned for 25–100 Gbit/s
Default timers misfired on this lab's 1 Gbit/s links.
A young ecosystem
Few tools and few deployments; even its dissector was stale.
Notes: Drawbacks, several measured in this lab: without priority queues the short-message advantage shrinks about 10x at the median; TCP wins big transfers because NIC offloads only understand TCP; the default timers misfire at 1 Gbit/s. grant_fifo_fraction reserves bandwidth for the oldest message and is 0 (off) in this build.

## Slide 9
TCP or Homa?
Homa fits RPC-heavy services inside one datacenter you control
 | TCP | Homa
Unit of data | a byte stream | a message (≤ 1 MB)
Setup | a connection per pair of machines | none
Who sets the pace | each sender, probing until loss | the receiver, with grants
Switch priority queues | not used | essential
Short messages under load | wait behind big transfers | overtake them
Big transfers | hardware offload, efficient | no offload; can be starved
Where it works | everywhere | inside one datacenter network
In Linux | since the beginning | out-of-tree; upstreaming in progress
Notes: When to use which. Homa makes sense for RPC-heavy services inside one datacenter whose owner controls hosts and switches, where tail latency is the problem. Across the internet, for bulk transfer, or with apps that can't change, TCP or QUIC remains the answer.

## Slide 10
PART 2
The lab
Four hosts, one switch with priority queues, a pinned build, and the tools to watch it work.
Notes: How the lab is put together, and why each piece is the way it is.

## Slide 11
Four hosts, one switch that matters
h1
192.168.80.11
h2
192.168.80.12
h3
192.168.80.13
h4
192.168.80.14
sw1
Linux bridge
1 Gbit/s · 8 queues
What runs where
Kernel 6.17.8, homa.ko, homa_prio and test servers on every host.
Each link is an isolated libvirt bridge, MTU 9000.
sw1 queues traffic on the way to each host — the receiver's downlink, where incast hits.
Hosts set link_mbps=1000 to match the bottleneck.
Notes: Each host-to-sw1 link is its own isolated libvirt bridge. sw1 bridges them and applies its egress policy on the way to each host, i.e. at the receiver's downlink, where incast congestion happens. The hosts set link_mbps=1000 so Homa sizes its pacing and grants for the real bottleneck (the default assumes 25 Gbit/s).

## Slide 12
One command builds and tests the module
./lab.sh image — about 10 minutes, then every VM is an overlay on the result
1
Pin
Hold the kernel packages; no background upgrades.
2
Kernel
Install mainline 6.17.8; boot it by name.
3
Build
homa.ko and util/ from the pinned commit.
4
Unit tests
840 tests, user-space harness: all pass.
5
Lab pieces
sw-qos, services, dissector; generalise.
Result kept in the image and checked by suite 01: unit tests: PASS (840 / 840 tests passed)
Notes: tools/build_image.sh boots a throwaway builder VM on libvirt's NAT network, runs image/homa-build.sh once, and powers off. The unit tests needed two definitions to compile against Ubuntu's mainline headers (no __seg_gs address space, CONFIG_TRACE_PREEMPT_TOGGLE); with them all 840 pass.

## Slide 13
One 300 KB RPC on the wire
Announced, granted, then sent — captured on sw1, decoded with the lab's dissector
0.000 ms h1 → h2 prio 7 66 B START_MSG 32843 → 4100 id=1219394 msg=300000
0.187 ms h2 → h1 prio 7 67 B GRANT 4100 → 32843 id=1219394 granted=200000 prio=0
0.327 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=0 len=8924 msg=300000
0.327 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=8924 len=8924 msg=300000
0.327 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=17848 len=8924 msg=300000
0.327 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=26772 len=8924 msg=300000
0.327 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=35696 len=8924 msg=300000
0.327 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=44620 len=8924 msg=300000
0.327 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=53544 len=8924 msg=300000
0.327 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=62468 len=8924 msg=300000
0.370 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=71392 len=8924 msg=300000
0.370 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=80316 len=8924 msg=300000
0.370 ms h1 → h2 prio 0 9014 B DATA 32843 → 4100 id=1219394 off=89240 len=8924 msg=300000
START_MSG
The sender announces 300,000 bytes and sends nothing else.
GRANT
0.2 ms later h2 allows 200,000 bytes, at priority 0.
DATA
Full 9 KB frames; more grants extend the window as data drains.
Notes: A 300 KB RPC captured on sw1's port to h1. The sender announces the message with START_MSG; the receiver grants 200,000 bytes one round trip later; data follows in full 9 KB frames and further grants extend the window. All grants say priority 0: with one message incoming, Homa uses the lowest scheduled priority. Capture on sw1, not the host: Homa's GRO handler consumes many arriving packets before tcpdump sees them.

## Slide 14
sw1 sorts Homa's packets by priority
Packets towards h1 during incast, by the priority in the IP header (thousands)
Chart: 
| priority 7 | priority 6 | priority 5 | priority 4 | priority 3 | priority 2 | priority 1 | priority 0
packets (thousands) | 54.9 | 167.9 | 1.8 | 0.5 | 0.1 | 0 | 0.1 | 0.5
Strict priority, by DSCP
Priority 7: short messages and all control packets — grants, acks, resends.
Priorities 6 and below: big messages' data, at the priority each grant names.
sw1 serves 7 first, then 6, and so on. TCP marks everything 0.
Notes: Packets leaving sw1 towards h1 during the Homa incast run, by the priority Homa wrote into the IP header. Priority 7 carries short messages and every control packet (grants, acks); 6 and below carry scheduled data at the priorities the grants assigned. sw1 serves them strictly in that order.

## Slide 15
PART 3
What the lab measured
Incast, Homa against TCP, loss recovery, and a finding about Homa's timers.
Notes: All numbers come from one collection run against the live lab, the same data as the PDF.

## Slide 16
Under incast, Homa's short messages overtake
100-byte probes into h1 while two senders saturate its port — round trip in ms, log scale
Chart: 
| Homa · priority queues | Homa · one FIFO | TCP · priority queues | TCP · one FIFO
median | 0.31 | 2.99 | 13 | 30.3
99th percentile | 1.53 | 6.07 | 21.8 | 38.4
0.31 ms
Homa median, priority queues
13 ms
TCP median, same queues
Notes: h2 and h3 stream 500 KB messages into h1, twice what its 1 Gbit/s port can take, while h4 sends 100-byte probes to h1. With priority queues Homa's probes overtake the queued bulk data: median 0.31 ms against 2.99 ms with one FIFO. TCP marks everything priority 0, so the queues can't help it: 13.0-30.3 ms. Idle probe RTT is about 0.15 ms. Log scale.

## Slide 17
Light load: a shorter tail, slower big transfers
Same workload over each protocol — 99th-percentile round trip in ms
Chart: 
| short ≤ 1 KB | medium 1–100 KB | long > 100 KB
Homa | 2.32 | 2.61 | 20.9
TCP | 4 | 4.09 | 15.9
Reading it
Short messages: Homa p99 2.32 ms, TCP 4.0 ms.
Medians are close: 0.29 vs 0.32 ms.
Long messages: TCP 15.9 ms, Homa 20.9 ms — TCP has NIC offload, Homa doesn't.
Notes: Light mixed load: Homa's W3 message-size distribution at 0.3 Gbit/s, about 170,000 RPCs each. Medians are close (short: Homa 0.29 ms, TCP 0.32 ms). Homa's p99 is lower for short and medium messages; TCP wins long messages because the virtio NICs give it segmentation offload and Homa gets none.

## Slide 18
Loss recovery without connections
sw1 drops 1 packet in 50 towards h1 while h2 runs 20 KB round trips
300/300
RPCs completed intact
19
RESENDs sent by h1
0
RPC timeouts
The receiver tracks which byte ranges of each message arrived and asks for the missing ones; the sender retransmits exactly those (20 packets). Nothing else to rebuild.
Notes: sw1 drops 1 in 50 packets towards h1, any type. h2 runs 300 round trips of 20 KB each way. Every RPC completes intact: h1 noticed the gaps and sent 19 RESENDs, h2 retransmitted 20 packets, nothing timed out. No connection state to repair.

## Slide 19
Finding: Homa's timers assume a fast network
Two senders into h1 at 1 Gbit/s, priority queues — default timers vs ×10
1
Parked
Shortest-first grants park the other messages at low priority.
2
Starved
Strict priority leaves them queued for tens of ms.
3
False alarm
After 5 ms of silence the receiver asks for queued data.
4
Overflow
The copies fill the queue: drops and timeouts.
Timers | sw1 drops | RESENDs | RPC timeouts | Bulk Mbit/s
Defaults: resend 5 ms, timeout 100 ms | 5814 | 2164 | 22 | 875
Scaled ×10: resend 50 ms, timeout 1000 ms | 0 | 302 | 0 | 877
Notes: The lab's own finding. Shortest-first grants park all but the leading message at low priorities; strict priority starves them for tens of milliseconds at 1 Gbit/s. After 5 ms of silence (resend_ticks) the receiver asks for data that is only queued; the copies overflow the same queue and RPCs time out. Homa's defaults assume 25-100 Gbit/s. Scaling resend_ticks, resend_interval and timeout_ticks by 10 removes the effect.

## Slide 20
26 tests, seven suites
./lab.sh test — about 12 minutes; the last full run passed 26 of 26
Suite | What it checks | Tests
01 platform | Pinned kernel, the right module build, unit tests passed, sysctls, services, sw1 | 5
02 function | Jumbo frames; 48 round trips v4/v6; 8 B–1 MB intact; unload and autoload | 5
03 wire | Packet types; short and control at priority 7; granted priorities below | 6
04 compare | Homa vs TCP on the same workload; Homa's short tail not worse | 2
05 incast | Priority queues help Homa; Homa beats TCP 10× at p50, 3× at p99 | 4
06 loss | 1/50 loss: all RPCs complete, RESENDs answered, no timeouts | 2
07 timers | Default timers misfire; ×10 timers: no drops, no timeouts | 2
Notes: ./lab.sh test runs seven Robot suites in about 12 minutes; the last full run passed all 26 tests. Suite 07 keeps the timer finding as a regression test.

## Slide 21
What we learned
Priority queues work
Under incast Homa's short messages stayed at 0.31 ms median; one FIFO: 2.99 ms; TCP: 13+ ms.
Scale the timers
At 1 Gbit/s the default resend timer misfires; ×10 removes drops and timeouts.
Offload gap
NICs segment TCP, not Homa; its GSO and TCP-hijack modes failed for 1 MB messages here.
Lab plumbing matters
UDP tunnels lost Homa's bursts silently; captures must be taken on the switch.
Notes: Summary of the findings. The priority-queue result reproduces Homa's central claim at small scale. The timer finding matters for anyone running Homa on slower links or emulating it. The offload and ecosystem points are the practical costs of adopting it today.

## Slide 22
What's next
1
Portal and metrics
A Prometheus exporter for Homa's metrics, a Grafana board, a portal on port 8108.
2
Upstream track
A second kernel built from the upstream Homa patches, compared with the module.
3
Offloads
Why GSO'd and TCP-hijacked large messages time out here.
4
Cluster benchmarks
HomaModule's cp_vs_tcp and cp_load adapted to four nodes.
Everything here is in ~/homa-lab — README, walkthrough PDF, and ./lab.sh to run it yourself.
Notes: Not built yet: portal and NMS integration, the upstream patch-series kernel as a second track, the offload investigation, and HomaModule's cluster benchmarks adapted to four nodes.